## Slide 1: An Audio Fingerprinting System for Live Version Identification using Image Processing Techniques
(Dr.?) Zafar Rafii
Northwestern University
EECS department

## Slide 2: Acknowledgments
Work done during internship at Gracenote, a company doing audio and video identification, with co-authors Bob Coover and Jinyu Han.
Work presented at the 39th IEEE International Conference on Acoustics, Speech and Signal Processing, Florence, Italy, May 4-9, 2014.

## Slide 3: Context
You are at a concert
  You know the artist who is playing
  You want to know about the song being played
  You have a smart device (e.g., an iPhone)

## Slide 4: Idea
You can use a music identification system
  You record an excerpt using your smart device
  It is processed and compared against a database
  You get information about the song (e.g., title)

## Slide 5: Principle
Audio fingerprinting systems
  Transform the audio into a compact fingerprint
  Compare the query against a database for a match
  Typically index fingerprints to speed up matching

## Slide 6: Limitations
Does not work with cover versions (e.g., live)
  Variations in tempo (e.g., faster renditions)
  Variations in key (e.g., higher pitch)
  Variations in instrumentations, etc.

## Slide 7: Solution
A novel system that can handle
  Short excerpt quickly (i.e., less than 10 seconds)
  Audio degradations (e.g., noise, encoding, etc.)
  Audio variations (e.g., different tempo, key, etc.)

## Slide 8: Approach
Fingerprinting stage
  Constant Q Transform
  Adaptive thresholding
Matching stage
  Hamming similarity
  Hough Transform

## Slide 9: Fingerprinting
Constant Q Transform (CQT)
  We first transform the audio signal into a time-frequency representation using the CQT
Time window centered at
24 seconds
Time frame centered at
24 seconds

## Slide 10: Fingerprinting
Constant Q Transform (CQT)
  The CQT has a log-frequency resolution, matching the notes of the chromatic scale (i.e., C, C#, etc.)
http://en.wikipedia.org/wiki/Note
Each note has the frequency
of the previous note
multiplied by
Logarithmic frequency resolution

## Slide 11: Fingerprinting
Constant Q Transform (CQT)
  Unlike the FT, the CQT is more compact and better adapted to music (vertical shift = pitch shift)
https://ccrma.stanford.edu/~gautham/
Three notes played at different pitches in
the FT-spectrogram (left) and the CQT-spectrogram (right)
Linear frequency resolution
Logarithmic frequency resolution

## Slide 12: Fingerprinting
Adaptive thresholding
  We transform the CQT-spectrogram into a binary image using an adaptive thresholding method

## Slide 13: Fingerprinting
Adaptive thresholding
  For each bin in the spectrogram, we assign 1 if the bin is higher than the median of the neighborhood
0
1
Neighborhood
at 25 seconds
and C4 (262 Hz)
Neighborhood
at 27 seconds
and C6 (1.0 kHz)
Bin
at 25 seconds
and C4 (262 Hz)
> than median
Bin
at 27 seconds
and C6 (1.0 kHz)
< than median

## Slide 14: Fingerprinting
+ energy
- energy
Adaptive thresholding
  We get a fingerprint that reduces the spectrogram into 2 components, of locally low and high energy
+ energy
- energy

## Slide 15: Approach
Fingerprinting stage
  Constant Q Transform
  Adaptive thresholding
Matching stage
  Hamming similarity
  Hough Transform

## Slide 16: Matching
Hamming similarity
  We then compute a similarity matrix between the fingerprints of a query and each of the references
Query fingerprint
Reference fingerprint
Similarity matrix
Matrix
multiplication
…
…
time
time
+ match
- match

## Slide 17: Matching
time
time
Hamming similarity
  We use the Hamming similarity between all pairs of time frames (= percentage of bins that match)
Query fingerprint
Reference fingerprint
Similarity matrix
Matrix
multiplication
…
…
Similarity between the time frames of the query and the reference
+ match
- match

## Slide 18: Matching
Hamming similarity
  We compute the similarity matrix for different pitch shifts between the query and the references
Similarity matrix
Matrix
multiplication
…
…
Reference fingerprint
time
Query fingerprint
time
Pitch shift down, one semitone
+ match
- match

## Slide 19: Matching
Hough Transform (HT)
  We binarize the similarity matrix via a threshold to have pairs of time frames that match (1) or not (0)
Query fingerprint
Reference fingerprint
Binarized similarity
…
…
time
time
match
no match

## Slide 20: Method
Hough Transform (HT)
  We use the HT to identify the best alignment between the query and the reference fingerprints
Query fingerprint
Reference fingerprint
Binarized similarity
…
…
time
time
Best alignment: 64% of time
frames matching
match
no match

## Slide 21: Matching
Hough Transform (HT)
  The HT helps to take into account potential tempo deviations, by trying different angles for a line
Query fingerprint
Reference fingerprint
Binarized similarity
…
…
time
time
Angle of 47°:
query slower
than reference
Angle of 45°:
query as fast
as reference
Angle of 41°:
query faster
than reference
match
no match

## Slide 22: Evaluation
References
  10 different artists of varied genres
  389 full tracks from studio albums
  Durations from 01’04’’ to 11’06’’
Queries
  87 full tracks from live albums (experiment 1)
  87 audio tracks from smart devices (experiment 2)
  10 queries per tracks, 6 and 9 second length

## Slide 23: Data set
artist | genre | #references | #queries
AC/DC | hard rock | 36 | 60
Arcade Fire | indie rock | 33 | 100
Bonobo | electronic | 42 | 100
Eagles | rock | 32 | 90
Foreigner | rock | 29 | 100
Jefferson Airplane | psychedelic rock | 65 | 40
Led Zeppelin | rock | 40 | 80
Phoenix | alternative rock | 38 | 100
Portishead | electronic | 33 | 100
Suprême NTM | French hip hop | 41 | 100
all | - | 389 | 870

## Slide 24: Live albums (9 seconds)
Top-k matches | k=1 | k=2 | k=3 | k=4 | k=5
AC/DC | 0.92 | 0.95 | 0.97 | 0.97 | 0.97
Arcade Fire | 0.84 | 0.92 | 0.94 | 0.96 | 0.97
Bonobo | 0.83 | 0.89 | 0.92 | 0.92 | 0.96
Eagles | 0.93 | 0.97 | 0.98 | 0.99 | 0.99
Foreigner | 0.88 | 0.93 | 0.93 | 0.95 | 0.97
Jefferson Airplane | 0.60 | 0.68 | 0.78 | 0.78 | 0.80
Led Zeppelin | 0.74 | 0.81 | 0.84 | 0.85 | 0.90
Phoenix | 0.88 | 0.92 | 0.93 | 0.97 | 0.98
Portishead | 0.92 | 0.93 | 0.93 | 0.93 | 0.93
Suprême NTM | 0.87 | 0.95 | 0.96 | 0.97 | 0.97
all | 0.86 | 0.91 | 0.92 | 0.94 | 0.95

## Slide 25: Smart devices (9 seconds)
Top-k matches | k=1 | k=2 | k=3 | k=4 | k=5
AC/DC | 0.70 | 0.83 | 0.85 | 0.87 | 0.93
Arcade Fire | 0.79 | 0.86 | 0.89 | 0.91 | 0.93
Bonobo | 0.60 | 0.75 | 0.83 | 0.89 | 0.93
Eagles | 0.70 | 0.77 | 0.88 | 0.91 | 0.91
Foreigner | 0.68 | 0.83 | 0.86 | 0.86 | 0.88
Jefferson Airplane | 0.40 | 0.53 | 0.55 | 0.60 | 0.63
Led Zeppelin | 0.28 | 0.39 | 0.48 | 0.53 | 0.54
Phoenix | 0.67 | 0.76 | 0.82 | 0.86 | 0.87
Portishead | 0.80 | 0.86 | 0.87 | 0.87 | 0.87
Suprême NTM | 0.30 | 0.42 | 0.45 | 0.51 | 0.55
all | 0.61 | 0.71 | 0.76 | 0.79 | 0.81